## Slide 1: Simple Mixing Using the Contaminant Transport Module
Rick Kossik
rkossik@goldsim.com

## Slide 2: GoldSim and the Contaminant Transport Module
  The basic GoldSim framework consists of a flexible set of tools for creating dynamic, probabilistic simulations of nearly any kind of complex system
    These tools are very abstract (like a programming language)
    They simply carry out mathematical calculations (e.g., numerical integration) that are applicable to many types of problems
    It is assumed you are familiar with the basic GoldSim framework
  In order to simulate some kinds of complex systems, such tools are not sufficient. Therefore, GoldSim has several specialized extension modules to facilitate simulation of some types of systems
  The Contaminant Transport Module is a set of specialized tools that are added to GoldSim to support complex contaminant transport simulations

## Slide 3: GoldSim and the Contaminant Transport Module
  The module is used to simulate the movement of mass (typically contaminants) through natural (and engineered) systems
  Produces predictions of mass transport rates at defined locations, concentrations in specified environmental media (e.g., water, soil), and impacts to defined human receptors (e.g., dose, health risk)
  Processes that can be simulated include mixing, solubility constraints, sorption, advection, dispersion, diffusion, and chemical reactions and radioactive decay and ingrowth
  This webinar will focus on simple mixing

## Slide 4: Overview of the Contaminant Transport Module

## Slide 5: Contaminant Transport Module
Adds specialized elements to facilitate simulation of contaminant transport through engineered and natural environmental systems

## Slide 6: Contaminant Transport Module
Provides a basic framework for modeling fate and transport of dissolved, sorbed and/or suspended contaminants through engineered and natural systems
Complexity of the model is determined by the user
While incorporating some basic physics (e.g., conservation of mass, decay and ingrowth, diffusion, partitioning), very few assumptions built into code in order to maximize flexibility
Heavily utilizes arrays

## Slide 7: Steps for Modeling Contaminant Transport
Specify species to be modeled
Specify the transport and storage media within the system to be modeled (e.g., water, air, sediment, soil)
Specify the transport pathways through which mass is transported and stored
Define the source terms (initial and/or boundary conditions)
Define the impacts of the species (e.g., dose) on defined receptors

## Slide 8: Defining Species
Species element

## Slide 9: Environmental Media
Basic “building blocks” of transport pathways
  mass transport calculations are based largely on media properties
  Two types: Fluids and Solids

## Slide 10: Transport Pathways
Transport pathways represent those parts of the system through which species mass is transported and/or in which species mass is stored.
  Tanks, ponds, aquifers, lakes, soil columns, etc.
You define the properties of the pathways, such as geometry, volume, and pathway discretization.
You define which media (e.g., air, water, sediments, rock) types are present in the pathway

## Slide 11: Transport Pathways
Pathways can be thought of as transfer functions
Each pathway type (or transfer function) assumes or represents a particular range of physical transport processes.

## Slide 12: Transport Pathways
You create a mass transport system by defining a network of transport pathways using mass flux links among the pathways.

## Slide 13: Transport Pathways
We will focus on Cells today to do simple mixing
We will also only consider water (no partitioning onto solids)
GoldSim provides five type of pathways:

## Slide 14: Pathways Mass Balance
Species mass is conserved.
The Contaminant Transport Module simulates mass transport so it solves for the mass of each species in each transport pathway.
  The water, or other media, balance is not a part of the transport module solution.
  Media amounts and advection rates are inputs (and not solution values) for transport pathways.
    You can link the transport media amounts and advection rates to a water balance model (or other media balance model) in order to enforce both a water balance and species mass balance.

## Slide 15: Let’s Look at Some Simple Mixing Models

## Slide 16: Cell Pathways
Act as mixing cells
Specify multiple media
  always contains a single reference fluid
Mass is instantly mixed and equilibrated (partitioned between media) within cell
Solubility constraints can be imposed in cell
Can have specified initial/boundary condition
Behavior of cell network is mathematically equivalent to network of finite difference nodes
We are not going to address multiple media or solubility today; just simple mixing

## Slide 17: Example1: Two Inflows into a Well-Mixed Flow-Through Tank
Tank holds 10 m3 of water
Initially concentration in the tank is 0 g/m3
4 m3/day of water with concentration of X of 10 g/m3 enters
6 m3/day of water with concentration of X of 2 g/m3 enters
10 m3/day of water leaves (volume stays constant)

## Slide 18: Example2: Two Inflows into a Well-Mixed Flow-Through Tank
Tank holds 10 m3 of water
Initially concentration in the tank is 20 g/m3
4 m3/day of water with concentration of X of 10 g/m3 enters
6 m3/day of water with concentration of X of 2 g/m3 enters
10 m3/day of water leaves (volume stays constant)

## Slide 19: Example3: Two Inflows into a Well-Mixed Flow-Through Tank
Vary tank volume from 0.1 m3 to 100 m3
Initially concentration in the tank is 0 g/m3
4 m3/day of water with concentration of X of 10 g/m3 enters
6 m3/day of water with concentration of X of 2 g/m3 enters
10 m3/day of water leaves (volume stays constant)

## Slide 20: Example4: Two Inflows into a Well-Mixed Flow-Through Tank
Small tank volume of 0.1 m3 (responds instantaneously)
Initially concentration in the tank is 0 g/m3
~4 m3/day (stochastic) of water with concentration of X of 10 g/m3 enters
~6 m3/day (stochastic) of water with concentration of X of 2 g/m3 enters
Same amount of water that enters leaves (volume stays constant)
This is analogous to computing the concentration at a point in a river where two streams meet (the point at which the two streams are instantaneously mixed)

## Slide 21: Example5: Two Inflows into a Well-Mixed Flow-Through Tank
Small tank volume of 0.1 m3 (responds instantaneously)
Initially concentration in the tank is 0 g/m3
~4 m3/day (stochastic) of water with concentration of X of 10 g/m3 and concentration of Y of 1 g/m3 enters
~6 m3/day (stochastic) of water with concentration of X of 2 g/m3 and concentration of Y of 3 g/m3 enters
Same amount of water that enters leaves (volume stays constant)
This is analogous to computing the concentration at a point in a river where two streams meet (the point at which the two streams are instantaneously mixed): Example6

## Slide 22: Example7
Assume 6 g/day of X is added to Pond1 for 5 days
Assume 10 g/day of X is added to Pond1 for 10 days
All ponds contain constant volume of 100 m3 of Water (hence, does not turn over immediately); the ponds are well-mixed
Water overflows from Pond1 and Pond2 to Pond3 and then out of system (to a “sink” Cell)
Pond2
Pond3
5 m3/day “Clean” water
10 g/day added for 10 days
Sink
Pond1
10 m3/day
5 m3/day “Clean” water
6 g/day added for 5 days

## Slide 23: Equations Solved by GoldSim
+
+
+ -
We have assumed Q and V to be constant, but they don’t have to be…

## Slide 24: Changing Flow Rates and Volumes
The previous examples treated the Cell(s) as having constant volume
This is because physically, they represented the following:
  A true constant volume entity (e.g., an overflowing tank or pond); or
  An infinitesimal slice of a system (e.g., the end of a reach in a stream)
But what if we wanted to compute mixing in a series of ponds or lakes (whose volume was not constant)?

## Slide 25: Example8
Assume 6 g/day of X is added to Pond1 for 5 days
Assume 10 g/day of X is added to Pond1 for 10 days
Pond1 and Pond2 have a constant volume of 100 m3 of Water (water overflows to Pond3)
Pond3 starts with 100 m3 of water. A pump turns on whenever volume exceeds 150m3 and turns off again when it is down to 100 m3 (and pumps at a rate of 15 m3/day)
Pond2
Pond3
5 m3/day “Clean” water
10 g/day added for 10 days
Sink
Pond1
variable
5 m3/day “Clean” water
6 g/day added for 5 days

## Slide 26: Summary
The Contaminant Transport Module can be used to easily carry out mixing calculations
  For simple systems, could do this without CT Module (with some additional effort)
Mixing calculations in GoldSim generally fall into two categories
  Computing concentrations at a specific point (e.g., in a river)
    Assume small constant volume
  Computing average concentrations in ponds or reservoirs
    Often need to model volume changes and slow turnover rates
    Do this by linking to flow model (e.g., made up or Pool or Reservoir elements)
    Note that volume should change slowly over a timestep to avoid numerical issues
What we have discussed here is very simple; the CT Module can do much more (e.g., solubility, partitioning, decay)
  But for many applications, a simple mixing model is appropriate

## Slide 27: Learn More
The Contaminant Transport Module is a complex and powerful add-on module for GoldSim
You can create extremely complex multi-dimensional models
Not intended to build highly discretized models
  In many cases, it can be argued that this is not necessary or appropriate
Best way to learn:
  User Manual
  Example models in Model Library
  Online Course (currently under construction)
  Send questions to GoldSim