## Slide 1: Simulating Flow Control
June 2025 GoldSim Webinar
By Jason Lillywhite

## Slide 2: What Is Flow Control?
Flow control is the process of actively managing the movement of water, energy, or materials through a system to maintain desired conditions.
It is used to:
  Maintain target levels (e.g., water in a reservoir, pressure in a pipe)
  Respond to changing conditions in real time
  Ensure system stability, safety, and efficiency
Common in:
  Water resource systems
  Industrial operations
  Environmental and energy systems

## Slide 3: Real-World Application: Water Balance Model
Model demonstration…

## Slide 4: Example Use Cases
Home thermostat (70° F set point)
  Heating turns on only if the temperature drops below 68°F.
  Heating stops if it rises above 72°F.
  No action is taken between 68–72°F.
PID Tank Level Control
  Maintains a precise temperature by adjusting fuel flow.
  Reacts not only to current error but also to how fast the temperature is changing and how long it has been off-target.
Image source: effykon.com
Image source: xtronics.com

## Slide 5: Feedback Control
Feedback control is a process where a system continuously monitors its output and adjusts its inputs to maintain a desired target or setpoint.
State Variable: What you want to control (e.g., pond level)
Controller: The logic that adjusts flows or actions
Target: The desired value or range
Feedback Loop: The system’s response to deviations
Controller
Process
Target
Error
Controller Output
Controller Properties

## Slide 6: Direction of Flow
Outflow Controller: Removes material when the process variable is too high.
Inflow Controller: Adds material when the process variable is too low.
Process variable increasing
Pump
Controller output: Increase signal
Process variable increasing
Pump
Controller output: Reduced signal
User must choose this before running the model. This will affect the direction of the response in the controller.
Inflow Type
Outflow Type

## Slide 7: Introducing the Controller Element
What is it?
  New in GoldSim 15.
  Designed to simulate feedback control systems.
Why it matters:
  Replaces complex logic with a single, intuitive element.
  Supports Deadband, Proportional, and PID control.
  Applicable across domains: water, energy, finance, etc.

## Slide 8: Controller Properties
Flow and Quantity Units
Process Variable
Flow Direction
Flow Capacity
Method
Target
Bias

## Slide 9: Types of Control
Choose the type before running the model
Choices:
  Deadband
  Proportional
  Proportional-Integral-Derivative (PID)

## Slide 10: Dead Band Control
Inputs
  Process Variable, Target, Direction, Max Flow capacity
  Target, Deadband Thickness, Target Position

## Slide 11: Target Position
Dead Band
Bottom
Target
Center
Top
Bottom
Target
Top
Top
Bottom
Target
Bottom
Top

## Slide 12: Proportional Control
Inputs
  Process Variable, Target, Direction, Max Flow capacity, Bias
  Proportional Gain Constant (Prop_Gain)
Output
  Min(max(Bias + Prop_Gain * Error, 0), Max flow)
  Proportional gain has dimensions of Bias / (error * time)

## Slide 13: PID Controller
Inputs
  Process Variable, Target, Direction, Max Flow capacity, Bias
  Tuning Factors:
    Proportional Gain (Prop_Gain) (1/T)
    Derivative Time Constant (Ti) (T)
    Integral time constant (Td) (1/T)
Output
  Output = min(max(P + I + D + Bias, 0), Max Flow)
  P = Prop_Gain * Error
  I = Error_Integral / Ti
  D = Td * (Error – Error_pv)

## Slide 14: Model Demonstrations
Compare outputs of different types

## Slide 15: Best Practices & Resources
When to use each control method.
Tips for tuning and testing.
Highlight learning resources:
  Help Documentation
  Online Course
  Model Library

## Slide 16: Questions?