## Slide 1: Introduction to the Contaminant Transport Module
Rick Kossik
rkossik@goldsim.com

## Slide 2: GoldSim and the Contaminant Transport Module
  The basic GoldSim framework consists of a flexible set of tools for creating dynamic, probabilistic simulations of nearly any kind of complex system
    These tools are very abstract (like a programming language)
    They simply carry out mathematical calculations (e.g., numerical integration) that are applicable to many types of problems
    It is assumed you are familiar with the basic GoldSim framework
  In order to simulate some kinds of complex systems, such tools are not sufficient. Therefore, GoldSim has several specialized extension modules to facilitate simulation of some types of systems
  The Contaminant Transport Module is a set of specialized tools that are added to GoldSim to support complex contaminant transport simulations

## Slide 3: GoldSim and the Contaminant Transport Module
  The module is used to simulate the movement of mass (typically contaminants) through natural (and engineered) systems
  Produces predictions of mass transport rates at defined locations, concentrations in specified environmental media (e.g., water, soil), and impacts to defined human receptors (e.g., dose, health risk)
  Processes that can be simulated include mixing, solubility constraints, sorption, advection, dispersion, diffusion, and chemical reactions and radioactive decay and ingrowth
  Can this be done with basic GoldSim?
    Simple mixing problems could be simulated, but any complex processes would be difficult or impossible to simulate without the Contaminant Transport Module

## Slide 4: There are Two Contaminant Transport Module Versions
  CT and RT
  RT includes several specialized features primarily used to simulate the transport of radionuclides (e.g., simulation of decay chains)

## Slide 5: What is the Contaminant Transport Module?
r
A set of specialized elements that are added to GoldSim to support complex contaminant transport simulations
RT Module Only

## Slide 6: Some Contaminant Transport Examples…

## Slide 7: Uranium Mine Closure

## Slide 8: Mine Water Treatment

## Slide 9: Shallow Disposal Facility

## Slide 10: Deep Disposal Facility

## Slide 11: Yucca Mountain

## Slide 12: How Detailed and Highly Discretized Should Your Contaminant Transport Model Be?
Just because you can build a large, highly discretized model does not mean you should
  How much uncertainty do you have in the source?
  How much uncertainty do you have in the key transport properties (e.g., partition coefficients, solubilities)?
  Do you really understand the dispersive characteristics of the system?
As a general rule, our ability to predict concentrations is much poorer (i.e., subject to greater uncertainty) than our ability to predict flows

## Slide 13: Since all models are wrong the scientist cannot obtain a "correct" one by excessive elaboration… Just as the ability to devise simple but evocative models is the signature of the great scientist, so overelaboration and overparameterization is often the mark of mediocrity. George Box, Science and Statistics (1976)

## Slide 14: Top-Down Modeling

## Slide 15: Overview of the Contaminant Transport Module

## Slide 16: Contaminant Transport Module
Adds specialized elements to facilitate simulation of contaminant transport through engineered and natural environmental systems
We will focus on only these five elements

## Slide 17: Contaminant Transport Module
Provides a basic framework for modeling fate and transport of dissolved, sorbed and/or suspended contaminants through engineered and natural systems
Complexity of the model is determined by the user
While incorporating some basic physics (e.g., conservation of mass, decay and ingrowth, diffusion, partitioning), very few assumptions built into code in order to maximize flexibility
Heavily utilizes arrays

## Slide 18: Steps for Modeling Contaminant Transport
Specify species to be modeled
Specify the transport and storage media within the system to be modeled (e.g., water, air, sediment, soil)
Specify the transport pathways through which mass is transported and stored
Define the source terms (initial and/or boundary conditions)
Define the impacts of the species (e.g., dose) on defined receptors

## Slide 19: Defining Species
Species element

## Slide 20: Environmental Media
Basic “building blocks” of transport pathways
  mass transport calculations are based largely on media properties
  Two types: Fluids and Solids

## Slide 21: Transport Pathways
Transport pathways represent those parts of the system through which species mass is transported and/or in which species mass is stored.
  Tanks, ponds, aquifers, lakes, soil columns, etc.
You define the properties of the pathways, such as geometry, volume, and pathway discretization.
You define which media (e.g., air, water, sediments, rock) types are present in the pathway

## Slide 22: Transport Pathways
Pathways can be thought of as transfer functions
Each pathway type (or transfer function) assumes or represents a particular range of physical transport processes.

## Slide 23: Transport Pathways
We will focus on Cells and Aquifers today
GoldSim provides five type of pathways:

## Slide 24: Transport Pathways
You create a mass transport system by defining a network of transport pathways using mass flux links among the pathways.

## Slide 25: Pathways Mass Balance
Species mass is conserved.
The Contaminant Transport Module simulates mass transport so it solves for the mass of each species in each transport pathway.
  The water, or other media, balance is not solved by the Contaminant Transport Module.
  Media advection rates and quantities are inputs for transport pathways.
    You can link the transport media advection rates to a water balance model (or other media balance model) in order to enforce both a water balance and species mass balance.

## Slide 26: Contaminant Sources
You can specify initial and boundary conditions in Pathways.
In some cases, however, direct specification of an initial condition or rate of input is not possible. The RT Module allows you to simulate a source term using a Source element. The Source element simulates:
  Failure of barriers containing the mass
  Degradation of matrix material (e.g., grout) in which the mass is bound
  Particularly useful when simulating engineered barrier systems
  Won’t discuss further

## Slide 27: Receptors
The objective of many studies is not only to compute contaminant concentrations and fluxes at various locations, but to also compute the impact of these contaminants on specified receptors.
GoldSim provides a Receptor element that facilitates the conversion of contaminant concentrations in media within pathways to impact to defined receptors (e.g., dose, health risk).
Won’t discuss further

## Slide 28: Let’s Look at Some Simple Models

## Slide 29: Cell Pathways
Act as mixing cells
Specify multiple media
  always contains a single reference fluid
Mass is instantly mixed and equilibrated (partitioned) within cell
Solubility constraints can be imposed in cell
Can have specified initial/boundary condition
Behavior of cell network is mathematically equivalent to network of finite difference nodes

## Slide 30: Mass Flux Links
Mass flux links connect pathway elements within a pathway network.
Behavior of a pathway network is primarily controlled by the manner in which mass flux links are defined.
Five types:
  Advective
  Diffusive
  Three special purpose types (will not discuss)
Multiple links can be made between/among pathways.
Mass fluxes are vectors by species with dimensions of mass/time.

## Slide 31: Example1: Simple Advection
Two well-mixed tanks filled with a fixed volume of water (V). Water flows through the tanks at a constant rate (Q) and is ultimately discharged to a sink.
A small quantity of contaminant X is initially introduced into Tank1. Tank2 initially has no mass.

## Slide 32: Equations Solved By GoldSim

## Slide 33: Example2: Advection with Partitioning
Add second species named Y (also added initially to Tank1)
Each Tank contains some sand
Y partitions onto the sand (X does not)
Assume sand mixes with water flowing through the tank (and there is instantaneous partitioning), but sand does not move with the water out of the tank

## Slide 34: Equations Solved by GoldSim

## Slide 35: Example3: Advection With Solubility
Two well-mixed tanks filled with a fixed volume of water (V). Water flows through the tanks at a constant rate (Q) and is ultimately discharged to a sink.
A small quantity of contaminant X and Y are initially introduced into Tank1. Tank2 initially has no mass.
X is infinitely soluble. Y has a solubility limit.
Note: this is a very simple way to represent solubility constraints, and a much more detailed approach accounting for the actual geochemical behavior is often necessary (e.g., linking dynamically or through lookup tables to a geochemical equilibrium code)

## Slide 36: How Does this Affect the Equations?

## Slide 37: Diffusive Mass Flux Links
Implements molecular diffusion among pathways.
Transport in a stagnant or slowly moving fluid via molecular diffusion
Diffusive flux is bi-directional (unlike advective links, mass can move in either direction). Mass will move from high concentration to low concentration, driven by the concentration gradient between the cells.

## Slide 38: Diffusive Mass Rate
Diffusive mass rate = dm/dt
(Diffusive Conductance) x (Concentration Difference)
Diffusive Conductance term is computed as follows:
    D = (A d t n r) / L
  where:
    D is the Diffusive Conductance (L3/T); A is the diffusive area (L2); d is the diffusivity in the fluid (L2/T); n is the porosity of the porous medium; t is the tortuosity of the porous medium; r is the Diffusivity Reduction (the default value is 1); and L is the total diffusive length (L).

## Slide 39: Example4: Diffusion
Cover exists on top of contaminated sediment at bottom of pond
Contaminated sediment is at a constant concentration
Contaminant must diffuse through cover to reach the pond

## Slide 40: Cells Can Represent Any Geometry

## Slide 41: How to Model Dispersion?
Aquifer Pathways

## Slide 42: Aquifer Pathway Element
Internally, GoldSim uses a series of Cells to create the Aquifer Pathway.
The Aquifer Pathway incorporates:
one-dimensional advection
longitudinal dispersion
Retardation (due to porous infill)
Decay and ingrowth
Transport on suspended particulates

## Slide 43: Example5: Cylinder - Aquifer Pathway
Horizontal cylinder filled with water and sand
Water flows through column at a fixed rate
Cl and Organic added at a constant rate
Organic partitions onto the sand (Cl does not)

## Slide 44: Combining Cells and Aquifers

## Slide 45: Coupling Flow and Transport Models
If the Flow is steady, no reason to model the flow system
If flow is transient, must couple these
  Use Reservoirs or Pools and Material Delays to model flow system
  Outputs of these elements are input to CT elements

## Slide 46: This is only the tip of the iceberg…
Many advanced features not discussed here:
  Transport on suspended particulates
  Water treatment (e.g., remove a certain fraction of incoming mass from a Cell)
  Other transport mechanisms (neither advective or diffusive): plant transport
  Matrix diffusion in fractures
  Linking to external transport models
  Simulation of complex source terms (the Source element)

## Slide 47: Summary
The Contaminant Transport Module is a complex and powerful add-on module for GoldSim
You can create extremely complex multi-dimensional models using only Cells and Aquifers
Not intended to build highly discretized models
  In many cases, it can be argued that this is not necessary or appropriate
Best way to learn:
  User Manual
  Example models in Model Library
  Online Course (currently under construction)

## Slide 49: Questions?