## Slide 1: Simulating One-Dimensional Advective-Dispersive Mass Transport
Rick Kossik
rkossik@goldsim.com

## Slide 2: The GoldSim Contaminant Transport Module
  The module is used to simulate the movement of mass (typically contaminants) through natural (and engineered) systems
  Produces predictions of mass transport rates at defined locations, concentrations in specified environmental media (e.g., water, soil), and impacts to defined human receptors (e.g., dose, health risk)
  Processes that can be simulated include mixing, solubility constraints, sorption, advection, dispersion, diffusion, and chemical reactions and radioactive decay and ingrowth
  This webinar focuses on those features that can be used to simulate one-dimensional advective-dispersive transport (e.g., in aquifers or streams)

## Slide 3: Outline
  Quick Overview of the Contaminant Transport Module
  What are the implications of the assumption of one-dimensional transport?
  Two ways to simulate one-dimensional transport:
    Aquifer Pathway
    Pipe Pathway
  Building Multi-Dimensional Models Using 1-D Pathways

## Slide 4: Overview of the Contaminant Transport Module

## Slide 5: What is the Contaminant Transport Module?
r
A set of specialized elements that are added to GoldSim to support complex contaminant transport simulations
RT Module Only
  Two versions of module: CT and RT
  RT includes several specialized features primarily used to simulate the transport of radionuclides (e.g., simulation of decay chains)

## Slide 6: Steps for Modeling Contaminant Transport
Specify species to be modeled
Specify the transport and storage media within the system to be modeled (e.g., water, air, sediment, soil)
Specify the transport pathways through which mass is transported and stored
Define the source terms (initial and/or boundary conditions)
Define the impacts of the species (e.g., dose) on defined receptors

## Slide 7: Transport Pathways
Transport pathways represent those parts of the system through which species mass is transported and/or in which species mass is stored.
  Tanks, ponds, aquifers, lakes, soil columns, streams, etc.
You define the properties of the pathways, such as geometry, volume, and pathway discretization.
You define which media (e.g., air, water, sediments, rock) types are present in the pathway

## Slide 8: Transport Pathways
Pathways can be thought of as transfer functions
Each pathway type (or transfer function) assumes or represents a particular range of physical transport processes.

## Slide 9: Transport Pathways
We will focus on Aquifers and Pipes today (but Cells will also make an appearance!)
GoldSim provides five type of pathways:

## Slide 10: Transport Pathways
You create a mass transport system by defining a network of transport pathways using mass flux links among the pathways.

## Slide 11: Implications of the One-Dimensional Transport Assumption

## Slide 12: Contaminant Plumes
Plumes spread longitudinally and transversely:
They also spread vertically:

## Slide 13: Contaminant Plumes
What are we typically trying to model when evaluating contaminant transport in a longitudinal feature such as an aquifer?
Are we interesting in predicting a concentration at some specific location?
  Typically, it is not realistic to do so (since actual plumes are extremely complex)
  Usually not necessary
Instead, we are often interested in a mass discharge rate (e.g., mass rate of discharge to a river, lake or well), and the subsequent concentration in that well-mixed location.

## Slide 14: Contaminant Plumes
A 1-D approach treats the system as a “tube”
It only treats longitudinal dispersion
But as such can be used to determine:
  When (and at what rate) does mass reach the discharge point
  The peak discharge rate, which determines peak concentrations in the discharge location (e.g., lake , pond)
Most appropriate if there is a primary discharge feature for the pathway (a river, a pond, a well) into which the plume discharges

## Slide 15: Aquifers and Pipes

## Slide 16: Aquifer Pathway Element
The Aquifer Pathway represents:
  one-dimensional advection, longitudinal dispersion, retardation, decay and ingrowth, transport on suspended particulates

## Slide 17: Aquifer Pathway Element
Internally, GoldSim uses a series of Cells to create the Aquifer Pathway.
The advective links are automatically generated in such a way to properly represent longitudinal dispersion (using a finite difference approximation)

## Slide 18: Pipe Pathways
Uses Laplace transforms to represent:
  one-dimensional advection, longitudinal dispersion, retardation, decay and ingrowth, transport on suspended particulates
  Can model matrix diffusion

## Slide 19: Comparison of Approaches
Pipes
  Can model matrix diffusion
  Cannot apply solubility limits within pathway
  Time-varying flow rates cannot be accurately modeled
Aquifers
  Cannot model matrix diffusion
  Can apply solubility limits within pathway
  All properties can change with time
As a general rule,
  Use Aquifer unless you need to simulate matrix diffusion
  Use Pipe if matrix diffusion is important
Limitations of both
  Flows should not change rapidly (best suited for steady flows)

## Slide 20: How Do You Define the Flow Area?
A 1-D pathway is essentially a tube.
But a plume is not a stream tube. That is, the cross-sectional area of the plume (and the flow rate in the plume) changes (generally increasing) with distance from source
So what values should we use for the Flow Area?
The Flow Area is actually somewhat arbitrary. As long as the Flow Rate and Flow Area are defined consistently (Q = KiA), they do not affect the mass breakthrough
  They do, however, affect the “average concentration” (which is almost never of interest).

## Slide 21: Computing Concentrations
Concentrations represent spatially-averaged concentration exiting the pathway
What if you want a concentration at a specific point?
  Of questionable value, but you can do this…
Plume function has eleven arguments
  Uses analytical solution to return a correction factor which can be used to multiply the Aquifer and Pipe concentration output
  This converts the spatially-averaged concentration to a concentration at an observation point

## Slide 22: Plume Function
Pathway Length (1)
Pathway cross-sectional Area
Source Length (2)
Depth (vertical distance) from the ground surface (or top of the flowing zone) to the observation point (3)
Horizontal (transverse) distance from the source center to the observation point (4)
Depth of the top of the source (5)
Width of the source (6)
Vertical thickness of the source (7)
Total thickness of the pathway being simulated (8)
Horizontal dispersivity
Vertical dispersivity

## Slide 23: Modeling Multi-Dimensional Systems

## Slide 24: How Detailed and Highly Discretized Should Your Contaminant Transport Model Be?
Just because you can build a large, highly discretized model does not mean you should
  How much uncertainty do you have in the source?
  How much uncertainty do you have in the key transport properties (e.g., partition coefficients, solubilities)?
  Do you really understand the dispersive characteristics of the system?
As a general rule, our ability to predict mass transport is much poorer (i.e., subject to greater uncertainty) than our ability to predict flows

## Slide 25: Since all models are wrong the scientist cannot obtain a "correct" one by excessive elaboration… Just as the ability to devise simple but evocative models is the signature of the great scientist, so overelaboration and overparameterization is often the mark of mediocrity. George Box, Science and Statistics (1976)

## Slide 26: Simple Multi-Dimensional System

## Slide 27: Shallow Disposal Facility

## Slide 28: Deep Disposal Facility

## Slide 29: Yucca Mountain

## Slide 30: Learn More
  User Manual
  Example models in Model Library
  Send questions to us!
  Online CT Course (currently under construction)